## Slide 1
Group 12
Song Yuchen, Shou Yiyang, Zeng Jialong, Qiu Huashen, Zheng Yixiao
Wireless Roadway Powered
Auto Guided Vehicle
Notes: We are group twelve and now I will introduce our project for you.

## Slide 2
Content
1 – Introduction
2 – Mechanical Design
3 – Circuit Design
4 – Software Design
5 – Problems Solving
6 – Future Improvements
Notes: Here are the contents. I will firstly make a quick overview of our project, and then introduce the detail design, and finally some problems and future improvements

## Slide 3
1-Introduction
A Simple Overview
Energy Transmission and Storage
- Moderate efficiency
Motion Control
- Smooth line tracking
Other Functions
- Self-starting when charging is cut
- Remaining energy display
- Count and broadcast number of loops
Notes: Here's a simple overview of our project. It has moderate efficiency for wireless energy transmission and storage. Its line tracking is relatively smooth. It also have some other functions such as self-starting when discharging, display the remaining energy, and count and broadcast the loops number.

## Slide 4
1-Introduction
Completion of Missions
Mission 1
- 60s charging, about 160J energy will be
stored in capacitors, and run 12 loops
Mission 2
- 60s charging, and then identify spots B,
C , D and stop to charge for 30s, and run
47.5 loops
Notes: For the first mission, we charge for 60 seconds and about 160 joules will be stored in capacitors, and it can run 12 loops. For the second mission, we first charge for 60 seconds and then stop at B, C and D to charge for 30 seconds. Finally it can run about 47.5 loops.

## Slide 5
2-Mechanical Design
Objective and Design
Adjustable
- Many holes to adapt different sizes
Light-Weighted
- Use lightweight materials such as nylon
nuts and wooden board
Notes: For the mechanical structure design, our main objectives are adjustable and light-weighted. So we make many holes to adapt for different module size and use lightweight materials such as nylon and wooden board.

## Slide 6
3-Circuit Design
Construction of WPT System
Transmitter
- 12V nominal input voltage
- Also workable with 10V input
Receiver
- 12V nominal output voltage
Notes: Here's the basic topological structure of our wireless power transfer system. For the two mission, we now use transmitter and receiver from Taobao with 12 volt nominal voltage. And it is also workable with 10 volt input.

## Slide 7
3-Circuit Design
Energy Storing and Using
Boost Converter
- Maximum output 2A
DC Motor
- Nominal voltage 6V
- Nominal current ≤ 0.16A
Buck-Boost Converter
- Input range 2~7V
Notes: To use the electrical energy in the capacitors, we first use a buck-boost converter to convert the voltage to 3.3 volt as the power supply for MCU and peripherals. And we also use a boost converter to convert the voltage to 6 volt to drive the motors. For the boost converter, its maximum output current is 2 ampere and since the nominal current of our motor less than 0.16 ampere, the converter is able to drive the motor.

## Slide 8
3-Circuit Design
Self-Starting Circuit
Charging
- Gate of MOSFET in high level
- Charging signal in low level
Not Charging
- Gate of MOSFET in low level
- Charging signal in high level
Notes: For the self-starting function. We made a simple circuit and use a signal to detect the charging status. For example, when the receiver is charging, the gate of mosfet will be in high level, and thus the charging signal will be low level. On the contrary, when the receiver is not in charging, the gate of mosfet will be low level, and thus the charging signal will be pull up to high level. By this way, MCU is able to know the charging status.

## Slide 9
3-Circuit Design
Voltage Divider
- Divider the voltage due to the input limitation of ADC
Notes: To display the voltage, we simply made a voltage divider circuit since there is limit for the ADC input voltage of MCU.

## Slide 10
3-Circuit Design
Some Attempts
Notes: We also made some attempt for the transmitter and receiver module. For example, this controllable transmitter that use a single mosfet to drive the LC resonance circuit. However, due to the time reason we haven't complete these part.

## Slide 11
4-Software Design
Line Tracking
- Two infrared sensors are used to detect the line
- Change the PWM duty cycle based on the track status
- Motor speed will be changed based on the PWM duty cycle

## Slide 12
4-Software Design
Counting Loops and Broadcasting
- Use one grayscale sensor to detect the blue spot
- MCU receives the ADC value from the sensor
- Loops = number of blue spots detected / 4
- MCU uses UART to send message to the broadcasting circuit, then convert the information to drive the module.

## Slide 13
4-Software Design
Display The Remaining Voltage
- Use ADC to read the value from voltage divider
- Then calculate the real remaining value of capacitors
- MCU send the predefined matrix to a low power consumption OLED screen through SPI, to display the remaining voltage

## Slide 14
5-Problems Solving
Program Flow Design
Notes: Okay, let me introduce the problem solving part to you.
But before that, let’s first have a brief look at the program flow.
When started, the peripherals begin to initialize, then the system will jump into the loop.
In the loop, there are two interruption procedures, the first one is by the signal from IR sensors, after that, it will start the line tracking procudure.
And the second onr is when the MCU detected signal from the charging module, it will stop and charge. We should notice that this event only takes place in the first three loops.
Finally, when it run out of power, the car stops.

## Slide 15
5-Problems Solving
Charging System
8.5V (180J)
8V (160J)
5.9V (174J)
9.1V (155J)
4.3V (138J)
- Series and parallel design of supercapacitor
Notes: We test different series and parallel combinations of capacitors we have, and record the receiving energy of each combination.
We found that there are two combinations with relatively high efficiency.
We use them as our final design.

## Slide 16
Gray scale
Infrared
5-Problems Solving
Line Tracking
Choosing Sensors
Real-Time Performance
Motor Speed Setting
- Sensitive to light condition
- Anti-interference
No interrupt
- Sometimes lose tracking
With interrupt
- Faster response
- Power consuming modules
Notes: For the task of line tracking, we faced some obstacles as well.
At first, we chose the analogue grey scale sensor for the lane tracking, but we soon found that it is very sensitive to the light condition of the surroundings.
So we changed to another type: digital infrared sensor, which works very stably.
For the real time issue, at the first stage check-up, we place the tracking code into the main function loop, but the car sometimes lose tracking, at the second stage check-up, however, we applied the technique of NVIC, it has faster response and robust line tracking ability then,
For the motor speed, as there are several peripherials consuming the power, we want to increase the motor speed as high as possible to reduce the relative power sonsumption of these peripherials.

## Slide 17
6-Future Improvements
Efficiency of wireless charging
Usage of supercapacitor electric energy
Power consumption of the MCU, peripherals, and motors
PID line tracking
Sleep mode of MCU
Notes: We have made a wireless charging Auto Guided Vehicle with moderate charging efficiency and well line tracking performance, together with some useful functions.
We also camp up with some ideas for future improvements.
We want to enhance the efficiency of wireless charging,
make full use of the supercapacitor energy, in other words, we want the remaining voltage of them as low as possible.
we also want to reduce the power consumption of the MCU peripherals, and motors, we may have a test of these devices from different brands
We will also adopt PID line tracking if we have more time
Also, we want to explore the sleep mode of MCU to better improve the performance of the car.

## Slide 18
Group 12
Song Yuchen, Shou Yiyang, Zeng Jialong, Qiu Huashen, Zheng Yixiao
Thanks!
Q & A
Notes: We are group twelve and now I will introduce our project for you.

## Slide 19
2
0
2
1
Group 12
Thanks for listening
Song Yuchen Shou Yiyang Zeng Jialong Qiu Huashen Zheng Yixiao